## Slide 1
SPI Communication Protocol
Presented by K. Sree Badrinath, Ch. Pranai and T. Obul Sai.
Notes: 1

## Slide 2
Introduction to SPI Communication
SPI (Serial Peripheral Interface) is a synchronous serial communication protocol. It's ideal for simple, short-distance communication. SPI is widely used in embedded systems for device interfacing.
Notes: 2

## Slide 4
SPI Basics: How it Works
Architecture
Single master controls one or more slaves in SPI communication.
  MOSI - Master Out Slave In
  MISO - Master In Slave Out
  SCK - Serial Clock
  SS/CS - Slave Select or Chip Select
Data Transmission
Master initiates transmission and controls the clock.
Supports full-duplex data exchange simultaneously.
Why Use SPI?
Provides high-speed communication for short-distance connections.
Simple hardware design with low pin count.
Allows multiple devices to be connected and controlled from a single master.
Notes: 3

## Slide 5
Advantages and Disadvantages of SPI
Advantages
  Simple to Implement: Protocol requires minimal hardware and coding effort.
  High Speed: Supports data rates over 100 Mbps for fast communication.
  Full-Duplex: Transmits and receives data simultaneously for efficiency.
  Flexible Format: Supports variable data lengths for diverse uses.
  Low Power: Efficient operation suits battery-powered gadgets.
Disadvantages
  Requires More Pins: Needs separate lines for each slave select, increasing wiring complexity.
  No Standardized Protocol: Lacks standardized message format, which may cause interoperability issues.
  Short Distance Only: Best suited for short-distance communication; not suitable for long cables.
  No Acknowledgment: No built-in error checking or acknowledgment mechanism.
  Limited Bus Length: Signal degradation limits the bus length and number of devices.
Notes: 4

## Slide 6
SPI Modes
SPI communication operates in four modes defined by clock polarity and phase.
Mode selection ensures correct data sampling and timing between master and slave.
Clock Polarity (CPOL)
Defines the idle state of the clock signal (high or low).
Clock Phase (CPHA)
Determines which clock edge data is sampled on—leading or trailing.
Modes Summary
  Mode 0: CPOL=0, CPHA=0
  Mode 1: CPOL=0, CPHA=1
  Mode 2: CPOL=1, CPHA=0
  Mode 3: CPOL=1, CPHA=1
Notes: 5

## Slide 7
SPI Modes
Parameters
  CPOL: Clock Polarity
  CPHA: Clock Phase
Modes define clock idle state and data sampling edge.
Four Modes
  Mode 0: CPOL=0, CPHA=0
  Mode 1: CPOL=0, CPHA=1
  Mode 2: CPOL=1, CPHA=0
  Mode 3: CPOL=1, CPHA=1
Master and slave must use the same mode for communication.
Notes: 6

## Slide 9
SPI Signal Timing Diagram
Key Signals
SCK clock controls data synchronization.
Setup and Hold
Data must be stable before and after clock edge.
Mode 0 Example
Data sampled on rising edge with clock idle low.
Notes: 7

## Slide 11
Common Applications of SPI
Peripheral Devices
  Temperature, pressure, accelerometer sensors
  EEPROM and Flash Memory
  Real-time clocks (RTC)
Additional Uses
  LCD and display interfaces
  ADC and DAC converters
  Inter-processor embedded communication
  SD card data transfer
Notes: 8

## Slide 12
Conclusion
Versatile and Widely Used
SPI fits many embedded communication needs.
Simple and Fast
Easy to implement with high data speed.
Understand Limitations
Account for short range and lack of error checks.
Choose Correct Mode
Matching clock settings ensures proper operation.
Notes: 9

## Slide 13
Thank You
We appreciate your attention to SPI communication protocol.
Notes: 10